APPROVED
by Resolution of the Cabinet of Ministers of Ukraine
No 355 of 24 May 2017

TECHNICAL REGULATION 
On Radio Equipment

General provisions

1. This Technical Regulation lays down requirements for radio equipment which is to be made available on the market and put into service in Ukraine and should apply to all forms of supply, including distance selling.

This Technical Regulation is based on Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC.

2. Such radio equipment shall not be covered by this Technical Regulation:

1) radioequipment used by radio amateurs in accordance with the Regulation on amateur radiocommunication of Ukraine, unless the equipment is made available on the market;

The following shall be regarded as not being made available on the market:

radiokits for assembly and use by radio amateurs;

radioequipment modified by and for the use of radio amateurs;

equipmentconstructed by individual radio amateurs for experimental and scientific purposes related to amateur radio;

2) marine equipment falling within the scope of the Technical Regulation on marine equipment, approved by the Resolution of the Cabinet of Ministers of Ukraine No 1103 of 5 September 2007 (Official Bulletin of Ukraine, 2007, No 67, p. 2588);

3) airborne products set out in point 51 of the first part of Article 1 of the Air Code of Ukraine;

4) custom-built kits destined to be used solely at research and development facilities.

3. This Technical Regulation shall not apply to radio equipment exclusively used for activities concerning public security, defence, State security, state border protection, criminal procedures and the functioning of the joint civil-military system of air traffic management of Ukraine.

4. Radio equipment falling within the scope of this Technical Regulation shall not be subject to:

Technical Regulation on Low-Voltage Electrical Equipment approved by the Resolution of the Cabinet of Ministers of Ukraine No 1067 of 16 December 2015 (Official Bulletin of Ukraine, 2015, No 102, p. 3526), except for the cases set out in the second paragraph of point 6 of this Technical Regulation;

Technical Regulation on Electromagnetic Compatibility of Equipment approved by the Resolution of the Cabinet of Ministers of Ukraine No 1077 of 16 December 2015 (Official Bulletin of Ukraine, 2016, No 2, p. 72), except for the cases set out in the third paragraph of point 6 of this Technical Regulation.

5. In this Technical Regulation, the terms below shall be used in the following meaning:

1) ‘accreditation of conformity assessment bodies’ (hereinafter referred to as ‘accreditation’) means an attestation by the state accreditation body of Ukraine that a conformity assessment body meets the requirements set by national standards, harmonized with the appropriate international and European standards, and, where applicable, any additional accreditation requirements including those set out in relevant sectoral schemes, to carry out a specific conformity assessment activity;

2) ‘putting into service’ means the first use of radio equipment for its intended use in Ukraine by its consumer (user);

3) ‘placing on the market’ means the first making available of radio equipment on the market of Ukraine;

4) ‘radio equipment class’ means a particular category of radio equipment which is considered similar in terms of the scope of its intended use;

5) ‘withdrawal’ means any measure aimed at preventing radio equipment in the supply chain from being made available on the market;

6) ‘manufacturer’ means any natural or legal person (either resident or non-resident of Ukraine) who manufactures radio equipment or has radio equipment designed or manufactured, and markets that equipment under his name or trade mark;

7) ‘recall’ means any measure aimed at achieving the return of radio equipment that has already been made available to the consumer (end-user);

8) ‘electromagnetic disturbance’ means any electromagnetic phenomenon which may degrade the performance of equipment. An electromagnetic disturbance may be electromagnetic noise, an unwanted signal or a change in the propagation medium itself;

9) ‘mark of conformity with technical regulations’ means a marking by which the manufacturer indicates that the radio equipment is in conformity with the applicable requirements set out in technical regulations providing for its affixing;

10) ‘importer’ means any natural or legal person, which is an economic operator resident in Ukraine, who places radio equipment from another country on the market of Ukraine;

11) ‘making available on the market’ means any supply of radio equipment for distribution, consumption or use on the market of Ukraine in the course of a commercial activity, whether in return for payment or free of charge;

12) ‘national accreditation body’ means the national accreditation body of Ukraine as defined in article 6 of Law of Ukraine “On Accreditation of Conformity Assessment Bodies”;

13) ‘conformity assessment body’ means an undertaking, institution, organization or their structural unit that performs conformity assessment activities, including testing, certification and inspection;

14) ‘conformity assessment’ means the process demonstrating whether the requirements of this Technical Regulation relating to radio equipment have been fulfilled;

15) ‘radiodetermination’ means the determination of the position, velocity and/or other characteristics of an object, or the obtaining of information relating to those parameters, by means of the propagation properties of radio waves;

16) ‘radiocommunication’ means electric communication by means of radio waves;

17) ‘radiointerface’ means a set of conditions of use of the radio equipment technology laid down in the Plan for the use of radiofrequency resource of Ukraine approved by Resolution of the Cabinet of Ministers of Ukraine No 815 of 9 June 2006 (Official Bulletin of Ukraine, 2006, No 24, p. 1771);

18) ‘radioequipment’ means an electrical or electronic product, which intentionally emits and/or receives radio waves for the purpose of radio communication and/or radiodetermination, or an electrical or electronic product which must be completed with an accessory so as to intentionally emit and/or receive radio waves for the purpose of radio communication and/or radiodetermination;

19) ‘radiowaves’ means electromagnetic waves of frequencies lower than 3 000 GHz, propagated in space without artificial guide;

20) ‘distributor’ means any natural or legal person in the radio equipment supply chain, other than the manufacturer or the importer, who makes radio equipment available on the market of Ukraine;

21) ‘economic operators’ means the manufacturer, the authorised representative, the importer and the distributor;

22) ‘technical specification’ means a document that prescribes technical requirements to be fulfilled by radio equipment;

23) ‘authorised representative’ means any natural or legal person resident in Ukraine who has received a written mandate from a manufacturer to act on his behalf in relation to specified tasks;

24) ‘harmful interference’ means interference which endangers the functioning of a radio navigation service or of other safety services or which otherwise seriously degrades, obstructs or repeatedly interrupts a radiocommunications service operating in accordance with the legislation;

In this Technical Regulation the terms “harmonised European standard”, “designating body”, “presumption of conformity”, “designation”, “risk” shall have the meanings as defined in the Law of Ukraine “On Technical Regulations and Conformity Assessment”; the term “improper use of the mark of conformity with technical regulations” — as defined in the Law of Ukraine “On State Market Surveillance and Control of Non-Food Products”; the terms “user”, “supply chain”, “supply of products” — as defined in the Law of Ukraine “On General Safety of Non-Food Products”; the term “national standard” — as defined in the Law of Ukraine “On Standardisation”.

Essential requirements

6. Radio equipment shall be constructed so as to ensure:

the protection of health and safety of persons and of domestic animals and the protection of property, including the objectives with respect to safety requirements set out in Technical Regulation on Low-Voltage Electrical Equipment approved by Resolution of the Cabinet of Ministers of Ukraine No 1067 of 16 December 2015, but with no voltage limit applying;

an adequate level of electromagnetic compatibility as set out in an adequate level of electromagnetic compatibility as set out in Technical Regulation on Electromagnetic Compatibility of Equipment approved by Resolution of the Cabinet of Ministers of Ukraine No 1077 of 16 December 2015.

7. Radioequipment shall be so constructed that it effectively uses and supports the efficient use of radio spectrum of Ukraine in the radio equipment technology concerned in order to avoid harmful interference.

In order to ensure the fulfilment of this requirement, radio equipment should be designed so that:

in the case of a transmitter, when the transmitter is properly installed, maintained and used for its intended purpose it generates radio waves emissions that do not create harmful interference, while unwanted radio waves emissions generated by the transmitter (e.g. in adjacent channels, out-of-band transmission, etc.) with a potential negative impact on the electromagnetic compatibility of radio equipment belonging to different categories of users of the radio spectrum of Ukraine should be limited to such a level that, according to the state of the art, harmful interference is avoided;

in the case of a receiver, it has a level of sensitivity, selectivity, and of other characteristics that allows it to operate as intended and to protect it against the risk of harmful interference, in particular from shared or adjacent channels, and from out-of-band transmissions, etc., and, in so doing, supports improvements in the efficient use of shared or adjacent channels and radio-frequency bands for the respective radio technology.

8. Radioequipment within certain categories or classes shall be so constructed that it complies with the following essential requirements:

1) radio equipment interworks with accessories, in particular with common chargers;

2) radio equipment interworks via networks with other radio equipment;

3) radio equipment can be connected to interfaces of the appropriate type throughout the territory of Ukraine;

4) radio equipment ensure the stable functioning of a network (connection of a device does not harm the network or its functioning nor misuse network resources, thereby causing an unacceptable degradation of service);

5) radio equipment ensures the protection of the personal data and privacy of users and of subscribers;

6) radio equipment supports certain features ensuring protection from fraud;

7) radio equipment supports certain features ensuring access to emergency services;

8) radio equipment supports certain features in order to facilitate its use by users with a disability;

9) radio equipment supports certain features in order to ensure that software can only be loaded into the radio equipment where the compliance of the combination of the radio equipment and software with the requirements of this Technical Regulation has been demonstrated.

The central body of the executive power in the field of communications shall specify in its legal acts which categories of radioequipment in the specific radio equipment technology are concerned by the requirements set out in subpoints 1 to 9 of this point.

Provision of information on the compliance of combinations of radio equipment and software

9. The NCRCI in accordance with Article 26 of the Law of Ukraine “On Radio Frequency Resource of Ukraine” shall determine whether the possibility of use of radioequipment, including its combination with software, affecting the compliance with essential requirements.

Registration of radio equipment affected by a low level of compliance with the essential requirements

10. Manufacturers shall provide the NCRCI with information on the radio equipment types affected by a low level of compliance with the essential requirements in order to register such radio equipment in the Register of radio-electronic equipment and emitting devices prior to radio equipment within those types being placed on the market. Such information shall contain the elements of technical documentation, referred to in Annex 4, except for subpoints 2 and 3 of point 1 of the mentioned Annex.

The NCRCI shall allocate to each registered radio equipment type a registration number, which manufacturers shall affix on radio equipment placed on the market as from 12 June 2018.

11. The NCRCI shall be empowered to adopt legal acts specifying which categories of radio equipment are concerned by the requirement set out in point 10 of this Technical Regulation, and the elements of the technical documentation to be provided to the NCRCI for such categories of radio equipment.

12. The NCRCI in accordance with the legislation shall lay down the operational rules for registration of radio equipment, for affixing the registration number on radio equipment and for maintenance of the Register of radio-electronic equipment and emitting devices.

Making available of radioequipment on the market

13. Radioequipment shall be made available on the market only if it complies with the requirements of this Technical Regulation.

Putting into service and use of radioequipment

14. Radioequipment shall be put into service and used if it complies with the requirements of this Technical Regulation, and when it is properly installed, maintained and used for its intended purpose.

Additional requirements for the putting into service and/or use of radio equipment for reasons related to the effective and efficient use of the radiofrequency resource of Ukraine, to the avoidance of harmful interference, to the avoidance of electromagnetic disturbances or to public health, shall be introduced by the Plan for the use of radiofrequency resource of Ukraine approved by Resolution of the Cabinet of Ministers of Ukraine No 815 of 9 June 2006.

Notification of radio interface specifications and conditions of use of radioequipment

15. In accordance with the Plan for the use of radiofrequency resource of Ukraine approved by Resolution of the Cabinet of Ministers of Ukraine No 815 of 9 June 2006 and upon a request of the NCRCI, the central body of the executive power in the field of communications shall make the information on radio interfaces publicly available at its website.

16. The NCRCI shall adopt the generalized conditions of use of radio equipment in the radio equipment technology concerned in accordance with its procedure.

Free movement of radioequipment

17. It is prohibited to impede, for reasons relating to aspects covered by this Technical Regulation, the making available on the Ukrainian market of radio equipment which complies with the requirements of this Technical Regulation.

18. At trade fairs, exhibitions and similar events, it is prohibited to create any obstacles to the display of radio equipment which does not comply with the requirements of this Technical Regulation, provided that a visible sign clearly indicates that such radio equipment may not be made available on the market or put into service until it has been brought into conformity with the requirements of this Technical Regulation. Demonstration of radio equipment may only take place provided that adequate measures, as prescribed by the NCRCI, have been taken to avoid harmful interference, electromagnetic disturbances and risk to the health or safety of persons or of domestic animals or to property.

Obligations of manufacturers

19. When placing their radio equipment on the market, manufacturers shall ensure that it has been designed and manufactured in accordance with the essential requirements.

20. Manufacturers shall ensure that radio equipment shall be so constructed that it can be operated in Ukraine as intended and without infringing applicable requirements on the use of radio spectrum of Ukraine.

21. Manufacturers shall draw up the technical documentation referred to in points 64 to 67 of this Technical Regulation and carry out one of the conformity assessment procedures set out in points 51 to 53 of this Technical Regulation, or have it carried out.

Where compliance of radio equipment with the applicable requirements of this Technical Regulation has been demonstrated by that conformity assessment procedure, manufacturers shall draw up a declaration of conformity according to Annex 5 and affix the mark of conformity with technical regulations.

22. Manufacturers shall keep the technical documentation and the declaration of conformity for 10 years after the last item of radio equipment has been placed on the market.

23. Manufacturers shall ensure that procedures are in place for series production of radio equipment to remain in conformity with the requirements of this Technical Regulation. Changes in radio equipment design or characteristics and changes in the standards from the list of the national standards referred to in point 49 of this Technical Regulation, or in other technical specifications by reference to which conformity of radio equipment is declared shall be adequately taken into account.

When deemed appropriate with regard to the risks presented by radio equipment, manufacturers shall, to protect the health and safety of consumers (end-users), carry out sample testing of radio equipment made available on the market, investigate, and, if necessary, keep a register of complaints, of non-conforming radio equipment and radio equipment recalls, and shall keep distributors informed of any such monitoring.

24. Manufacturers shall ensure that the radio equipment which they have placed on the market bears a type, batch or serial number or other element allowing its identification, or, where the nature of the radio equipment does not allow it, that the required information is provided on the packaging, or in document accompanying the radio equipment.

25. Manufacturers shall indicate on the radio equipment their name, registered trade name or registered trade mark and the postal address at which they can be contacted or, where the size or nature of radio equipment does not allow it, on its packaging, or in a document accompanying the radio equipment. The address shall indicate a single point at which the manufacturer can be contacted. The contact details shall be provided in accordance with the law on the order of application of languages.

26. Manufacturers shall ensure that the radio equipment is accompanied by instructions and safety information in accordance with the law on the order of application of languages.

Instructions shall include the information required to use radio equipment in accordance with its intended use. Such information shall include, where applicable, a description of accessories and components, including software, which allow the radio equipment to operate as intended. Such instructions and safety information, as well as any labelling, shall be clear, understandable and intelligible.

The following information shall also be included in the instruction in the case of radio equipment intentionally emitting radio waves:

frequency band(s) in which the radio equipment operates;

maximum radio-frequency power transmitted in the frequency band(s) in which the radio equipment operates.

27. Manufacturers shall ensure that each item of radio equipment is accompanied by a copy of the declaration of conformity or by a simplified declaration of conformity. Where a simplified declaration of conformity, a blank-form of which is set out in Annex 6, is provided, it shall contain the exact internet address where the full text of the declaration of conformity can be obtained.

28. In cases of requirements for authorisation of use of radio equipment, the manufacturer shall be obliged to provide the information specified by the NCRCI in the documents accompanying the radio equipment, or on the packaging, or in the declaration of conformity.

The NCRCI may adopt legal acts specifying how to present information of the existing requirements for authorisation of use of radio-electronic equipment and the other parameters for the use of radio spectrum of Ukraine.

29. Manufacturers who consider or have reason to believe that radio equipment which they have placed on the market is not in conformity with this Technical Regulation shall immediately take the corrective measures necessary to bring that radio equipment into conformity, to withdraw it or recall it, if appropriate. Furthermore, where the radio equipment presents a risk, manufacturers shall immediately inform the state market surveillance authorities, giving details, in particular, of the noncompliance of such radio equipment with the Technical Regulation, of any corrective measures taken and of the results thereof.

30. Manufacturers shall, further to a reasoned request from a state market surveillance authority, provide it with all the information and documentation (in paper or electronic form) necessary to demonstrate the conformity of the radio equipment with this Technical Regulation. Manufacturers shall cooperate with that authority, at its request, on any action taken to eliminate the risks posed by radio equipment which they have placed on the market.

Authorised representatives

31. A manufacturer may, if necessary, by a written mandate (agreement, power of attorney, etc.), appoint an authorised representative.

The obligations of manufacturer laid down in point 19 of this Technical Regulation and the obligation of manufacturer to draw up technical documentation laid down in point 21 of this Technical Regulation shall not form part of the authorised representative’s mandate.

32. An authorised representative shall perform the tasks specified in the mandate allowing the authorised representative to do at least the following:

keep the declaration of conformity and the technical documentation at the disposal of market surveillance authorities for 10 years after the radio equipment has been placed on the market;

further to a reasoned request from a state market surveillance authority, provide that authority with all the information and documentation necessary to demonstrate the conformity of radio equipment;

further to a reasoned request from a state market surveillance authority, cooperate with that authority on any action taken to eliminate the risks posed by radio equipment covered by the authorised representative’s mandate.

Obligations of importers

33. Importers shall place on the market only that radio equipment which complies with the requirements of this Technical Regulation.

34. Before placing radio equipment on the market importers shall ensure that:

the appropriate conformity assessment procedure referred to in points 51 to 53 of this Technical Regulation has been carried out by the manufacturer;

that the radio equipment is so constructed that it can be operated without infringing applicable requirements on the use of radio spectrum of Ukraine;

the manufacturer has drawn up the technical documentation;

the radio equipment bears the mark of conformity with technical regulations and is accompanied by the information and documents referred to in points 26 to 28 of this Technical Regulation;

the manufacturer has complied with the requirements set out in points 24 and 26 of this Technical Regulation.

Where an importer considers or has reason to believe that radio equipment is not in conformity with the essential requirements, he shall not place the radio equipment on the market until it has been brought into conformity. Furthermore, where the radio equipment presents a risk, the importer shall inform the manufacturer and the state market surveillance authorities to that effect.

35. Importers shall indicate on the radio equipment their name, registered trade name or registered trade mark (mark for goods and services) and the postal address at which they can be contacted or, where that is not possible, on its packaging or in a document accompanying the radio equipment.

The contact details shall be provided in accordance with the law on the order of application of languages.

36. Importers shall ensure that the radio equipment is accompanied by instructions and safety information in the form compliant with the requirements of law on the order of application of languages.

37. Importers shall ensure that, while radio equipment is under their responsibility, its storage or transport conditions do not jeopardise its compliance with the essential requirements.

38. When deemed appropriate with regard to the risks presented by radio equipment, importers shall, to protect the health and safety of consumers (end-users), carry out sample testing of radio equipment made available on the market, investigate, and, if necessary, keep a register of complaints, of non-conforming radio equipment and radio equipment recalls, and shall keep distributors informed of any such monitoring.

39. Importers who consider or have reason to believe that radio equipment which they have placed on the market is not in conformity with this Technical Regulation shall immediately take the corrective measures to bring that radio equipment into conformity with the mentioned requirements, to withdraw it or recall it, if appropriate. Furthermore, where the radio equipment presents a risk, importers shall immediately inform the state market surveillance authorities giving details of the non-compliance and of any corrective measures taken.

40. Importers shall, for 10 years after the radio equipment has been placed on the market, keep a copy of the declaration of conformity at the disposal of the state market surveillance authorities and ensure that the technical documentation can be made available to those authorities, upon request.

41. Importers shall, further to a reasoned request from a state market surveillance authority, provide it with all the information and documentation (in paper or electronic form) necessary to demonstrate the conformity of the radio equipment with this Technical Regulation. Importers shall cooperate with that authority, at its request, on any action taken to eliminate the risks posed by radio equipment which they have placed on the market.

Obligations of distributors

42. When making radio equipment available on the market distributors shall act with due care in relation to the requirements of this Technical Regulation.

43. Before making radio equipment available on the market distributors shall verify that the radio equipment bears the mark of conformity with technical regulations, that it is accompanied by the documents required by this Technical Regulation and by the instructions and safety information in the form compliant with the requirements of legislation on the order of application of languages, and that the manufacturer and the importer have complied with the requirements set out in points 20,  24 to 28, and 35 of this Technical Regulation.

Where a distributor considers or has reason to believe that radio equipment is not in conformity with the essential requirements, he shall not make the radio equipment available on the market until it has been brought into conformity.

Furthermore, where the radio equipment presents a risk, the distributor shall inform the manufacturer or the importer to that effect as well as the state market surveillance authorities.

44. Distributors shall ensure that, while radio equipment is under their responsibility, its storage or transport conditions do not jeopardise its compliance with the essential requirements.

45. Distributors who consider or have reason to believe that radio equipment which they have made available on the market is not in conformity with this Technical Regulation shall make sure that the corrective measures necessary to bring that radio equipment into conformity, to withdraw it or recall it, if appropriate, are taken. Furthermore, where the radio equipment presents a risk, distributors shall immediately inform the market surveillance authorities, giving details, in particular, of the non-compliance and of any corrective measures taken.

46. Distributors shall, further to a reasoned request from a state market surveillance authority, provide it with the information and documentation (in paper or electronic form) necessary to demonstrate the conformity of the radio equipment with this Technical Regulation. They shall cooperate with that state market surveillance authority, at its request, on any action taken to eliminate the risks posed by radio equipment which they have made available on the market.

Cases in which obligations of manufacturers apply to importers and distributors

47. An importer or distributor shall be considered a manufacturer for the purposes of this Technical Regulation and he shall be subject to the obligations of the manufacturer under points 19 to 30 of this Technical Regulation, where the compliance of radio equipment with this Technical Regulation may be affected, namely where they:

place radio equipment on the market under their name or trade mark (mark for goods and services);

modify radio equipment already placed on the market.

Identification of economic operators

48. Economic operators shall, on request, identify the following to the market surveillance authorities:

any economic operator who has supplied them with radio equipment;

any economic operator to whom they have supplied radio equipment.

Economic operators shall be able to present the information referred to in the first to the third paragraphs of this point for 10 years after they have been supplied with the radio equipment and for 10 years after they have supplied the radio equipment.

Presumption of conformity of radio equipment

49. The list of standards from the list of the national standards which are identical to the relevant harmonised European standards to provide radio equipment with presumption of conformity with the essential requirements (hereinafter referred to as the “list of the national standards”) shall be adopted and published in accordance with Article 11 of the Law of Ukraine “On Technical Regulations and Conformity Assessment”.

Radio equipment which is in conformity with standards from the list of the national standards or parts thereof shall be presumed to be in conformity with the essential requirements covered by those standards or parts thereof.

Conformity assessment procedures

50. The manufacturer shall perform a conformity assessment of the radio equipment with a view to meeting the essential requirements. The conformity assessment shall take into account all intended operating conditions and, for the essential requirement set out in the second paragraph of point 6 of this Technical Regulation, the assessment shall also take into account the reasonably foreseeable conditions. Where the radio equipment is capable of taking different configurations, the conformity assessment shall confirm whether the radio equipment meets the essential requirements in all possible configurations.

51. The manufacturer shall demonstrate compliance of radio equipment with the essential requirements set out in point 6 of this Technical Regulation using any of the following conformity assessment procedures:

internal production control set out in Annex 1;

type examination that is followed by the conformity to type based on internal production control set out in Annex 2;

conformity based on full quality assurance set out in Annex 3.

52. Where, in assessing the compliance of radio equipment with the essential requirements set out in points 7 and 8 of this Technical Regulation, the manufacturer has applied standards from the list of the national standards, he may use any of the following procedures:

internal production control set out in Annex 1;

type examination that is followed by the conformity to type based on internal production control set out in Annex 2;

conformity based on full quality assurance set out in Annex 3.

53. Where, in assessing the compliance of radio equipment with the essential requirements set out in points 7 and 8 of this Technical Regulation, the manufacturer has not applied or has applied only in part standards from the list of the national standards, or where such standards do not exist for such class of radio equipment, he may use any of the following procedures:

type examination that is followed by the conformity to type based on internal production control set out in Annex 2;

conformity based on full quality assurance set out in Annex 3.

Declaration of conformity

54. The declaration of conformity shall state that the fulfilment of the essential requirements has been demonstrated.

55. The declaration of conformity shall have the model structure set out in Annex 5.

The declaration of conformity shall contain the elements set out in Annex 5 and shall be continuously updated.

The declaration of conformity shall be drawn up in the official language, and where it had been drawn up in another language - it shall be translated into the official language.

The simplified declaration of conformity referred to in point 27 of this Technical Regulation shall contain the elements set out in Annex 6 and shall be continuously updated. The full text of the declaration of conformity in the official language shall be available at the internet address referred to in the simplified declaration of conformity.

56. Where radio equipment is subject to more than one technical regulation requiring a declaration of conformity, a single declaration of conformity shall be drawn up in respect of all such technical regulations. That declaration of conformity shall contain the identification of the technical regulations concerned including their publication references.

The single declaration of conformity may be a dossier made up of relevant individual declarations of conformity.

57. By drawing up the declaration of conformity, the manufacturer shall assume responsibility for the compliance of the radio equipment with the requirements laid down in this Technical Regulation.

General principles of marking with the mark of conformity with technical regulations

58. The general principles of marking with the mark of conformity with technical regulations are set out in Article 30 of the Law of Ukraine “On Technical Regulations and Conformity Assessment”.

59. On account of the nature of radio equipment, the height of the mark of conformity with technical regulations affixed to radio equipment may be lower than 5 mm, provided that it remains visible and legible.

Rules and conditions for affixing the mark of conformity with technical regulations and the identification number of the designated body

60. The mark of conformity with technical regulations shall be affixed visibly, legibly and indelibly to the radio equipment, or, if that is not possible, to its data plate. The mark of conformity with technical regulations shall also be affixed visibly and legibly to the packaging.

61. The mark of conformity with technical regulations shall be affixed before the radio equipment is placed on the market.

62. The mark of conformity with technical regulations shall be followed by the identification number of the designated conformity assessment body (hereinafter referred to as the “designated body”) where the conformity assessment procedure set out in Annex 3 was applied.

The identification number of the designated body shall have the same height as the mark of conformity with technical regulations. The identification number of the designated body shall be affixed by the designated body itself or, under its instructions, by the manufacturer or his authorised representative.

63. Restrictive (corrective) measures in the event of improper use of the mark of conformity with technical regulations shall be applied in accordance with the legislation.

Technical documentation

64. The technical documentation shall contain all relevant data or details of the means used by the manufacturer to ensure that radio equipment complies with the essential requirements. The contents of the technical documentation is set out in Annex 4.

65. The technical documentation shall be drawn up before radio equipment is placed on the market and shall be continuously updated.

66. Where the technical documentation and correspondence relating to any type examination procedure is drawn up in a language that is different from the official language, economic operators shall, further to a reasoned request from designated bodies, be obliged to have at their own expense and within a period agreed with such bodies the technical documentation and correspondence translated into the official language to the extent required. By agreement of the parties, the technical documentation may be provided in the language in which the technical documentation was drawn up.

67. Where the technical documentation does not comply with points 64 to 66 of this Technical Regulation, and in so doing fails to present sufficient relevant data or means used to ensure compliance of radio equipment with the essential requirements, the state market surveillance authority may ask the manufacturer or the importer to have a test performed by a conformity assessment body acceptable to the state market surveillance authority at the expense of the manufacturer or the importer within a specified period in order to verify compliance with the essential requirements.

Designation of conformity assessment bodies

68. The designation of conformity assessment bodies and the execution of third-party conformity assessment tasks by them under this Technical Regulation shall be carried out in accordance with the Law of Ukraine “On Technical Regulations and Conformity Assessment”.

Requirements relating to designated bodies

69. In order to be designated a conformity assessment body shall meet the general requirements to designated bodies according to Article 32 of the Law of Ukraine “On Technical Regulations and Conformity Assessment”, as well as the special requirements to designated bodies laid down in points 70 to 77 of this Technical Regulation.

70. A conformity assessment body shall be a third-party body independent of the organisation or the radio equipment it assesses.

A conformity assessment body belonging to a business association or professional federation representing legal entities and/or individual entrepreneurs involved in the design, manufacturing, provision, assembly, use or maintenance of radio equipment which it assesses may, on condition that its independence and the absence of any conflict of interest are demonstrated, be considered as a third-party body.

71. A conformity assessment body, its top level management and the personnel responsible for carrying out the conformity assessment tasks shall not:

be the designer, manufacturer, supplier, installer, purchaser, owner, user or maintainer of the radio equipment which they assess, nor the representative of any of those parties. This shall not preclude the use of assessed radio equipment that is necessary for the operations of the conformity assessment body or the use of such radio equipment for personal purposes;

be directly involved in the design, manufacture or construction, the marketing, installation, use or maintenance of that radio equipment, or represent the parties engaged in those activities. They shall not engage in any activity that may conflict with their independence of judgement or integrity in relation to conformity assessment activities for which they are designated. This shall in particular apply to consultancy services.

Conformity assessment bodies shall ensure that the activities of their subsidiaries or subcontractors, which are engaged in the conformity assessment activities by such bodies, do not affect the confidentiality, objectivity or impartiality of their conformity assessment activities.

72. Conformity assessment bodies and their personnel shall carry out the conformity assessment activities with the highest degree of professional integrity and the requisite technical competence in the specific field and shall be free from all pressures and inducements, particularly financial, which might influence their judgement or the results of their conformity assessment activities, especially as regards persons or groups of persons with an interest in the results of those activities.

73. A conformity assessment body shall be capable of carrying out all the conformity assessment tasks assigned to it by Annexes 2 and 3 in relation to which it has been designated, whether those tasks are carried out by the conformity assessment body itself or on its behalf and under its responsibility.

At all times and for each conformity assessment procedure and each class of radio equipment in relation to which it has been designated, a conformity assessment body shall have at its disposal the necessary:

personnel with technical knowledge and sufficient and appropriate experience to perform the conformity assessment tasks;

descriptions of procedures for each class of radio equipment in accordance with which conformity assessment is carried out, ensuring the transparency and the ability of reproduction of those procedures; A conformity assessment body shall have appropriate policies and procedures in place that distinguish between tasks it carries out as a designated body and other activities;

procedures for the performance of activities which take due account of the size of an undertaking, the sector in which it operates, its structure, the degree of complexity of radio equipment technology in question and the mass or serial nature of the production process.

A conformity assessment body shall have the means necessary to perform the technical and administrative tasks connected with the conformity assessment activities in an appropriate manner.

74. The personnel responsible for carrying out conformity assessment tasks shall have the following:

sound technical and vocational training covering all the conformity assessment activities in relation to which the conformity assessment body is designated of has been designated;

satisfactory knowledge of the requirements of the assessments they carry out and adequate authority to carry out those assessments;

appropriate knowledge and understanding of the essential requirements set out in points 6 to 8 of this Technical Regulation, the order of application and the scope of standards from the list of the national standards, and of the relevant provisions of the Ukrainian legislation and the EU legislation concerning the conditions of use, making available on the market and putting into service of radio equipment which it assesses;

the ability to draw up type examination certificates and/or quality system approvals, records and reports demonstrating that assessments have been carried out.

75. The impartiality of the conformity assessment bodies, their top level management and of the personnel responsible for carrying out the conformity assessment tasks shall be guaranteed.

The remuneration of the top level management and personnel responsible for carrying out the conformity assessment tasks of a conformity assessment body shall not depend on the number of assessments carried out or on the results of those assessments.

76. The personnel of a conformity assessment body shall observe professional secrecy with regard to all information obtained in carrying out their tasks under Annexes 2 and 3, except for the cases specified by the legislation in relation to the authorised authorities, and protect the proprietary data of economic operators.

77. Conformity assessment bodies shall participate in, or ensure that their personnel responsible for carrying out the conformity assessment tasks are informed of, the relevant standardisation activities.

Designated bodies shall participate in the relevant activities of the sectoral group of designated bodies in accordance with point 90 of this Technical Regulation, and ensure that their personnel responsible for carrying out the conformity assessment tasks are informed of such activities, and shall apply as general guidance the administrative decisions and documents produced as a result of the work of that group.

Subsidiaries of and subcontracting by designated bodies

78. Where a designated body subcontracts specific tasks connected with conformity assessment or has recourse to a subsidiary, it shall ensure that the subcontractor or the subsidiary meets the requirements set out in points 69 to 77 of this Technical Regulation and shall inform the designating authority accordingly.

79. Designated bodies shall take full responsibility for the tasks performed by subcontractors or subsidiaries wherever these are established.

80. Activities may be subcontracted or carried out by a subsidiary only with the agreement of the client.

81. Designated bodies shall keep at the disposal of the designating authority the relevant documents concerning the assessment of the qualifications of the subcontractor or the subsidiary and the work carried out by them under Annexes 2 and 3.

Operational obligations of designated bodies

82. Designated bodies shall carry out conformity assessments in accordance with the conformity assessment procedures provided for in Annexes 2 and 3.

83. Conformity assessments shall be carried out avoiding unnecessary burdens for economic operators, taking due account of the sector in which it operates, its characteristics, namely, its structure, the degree of complexity of the radio equipment technology in question and the mass or serial nature of the production process.

In so doing they shall nevertheless respect the degree of rigour and the level of protection required for the compliance of the radio equipment with this Technical Regulation.

84. Where a designated body finds that the essential requirements or the requirements set out in corresponding standards from the list of the national standards or other technical specifications have not been met by a manufacturer, it shall require that manufacturer to take appropriate corrective measures and shall not issue a type examination certificate or a quality system approval.

85. Where, in the course of the monitoring of conformity following the issue of a type examination certificate or a quality system approval, a designated body finds that radio equipment no longer complies with the essential requirements, it shall require the manufacturer to take appropriate corrective measures and shall suspend or withdraw the type examination certificate or the quality system approval if necessary.

86. Where corrective measures are not taken or do not have the required effect, the designated body shall restrict, suspend or withdraw any type examination certificates or quality system approvals, as appropriate.

Appeal against decisions of designated bodies

87. Appeals against decisions of designated bodies shall be submitted and considered under the requirements of Article 43 of the Law of Ukraine “On Technical Regulations and Conformity Assessment”.

Information obligation on designated bodies

88. Designated bodies shall provide the designating authority with the information specified in Article 42 of the Law of Ukraine “On Technical Regulations and Conformity Assessment”.

89. Designated bodies shall, in accordance with the requirements of Annexes 2 and 3, provide the other conformity assessment bodies designated under this Technical Regulation carrying out similar conformity assessment activities covering the same categories of radio equipment with relevant information on issues relating to negative and, on request, positive conformity assessment results.

Coordination of designated bodies

90. There shall be ensured that appropriate coordination and cooperation between conformity assessment bodies designated under this Technical Regulation are put in place and properly operated in the form of a sectoral group of designated bodies.

Designated bodies shall participate in the work of the sectoral group, directly or by means of designated representatives.

State market surveillance and state control of radio equipment

91. The state market surveillance and state control of radio equipment shall be carried out in accordance with the Law of Ukraine “On State Market Surveillance and Control of Non-Food Products” taking into account the special requirements laid down in points 92 to 96 of this Technical Regulation.

92. Where the state market surveillance authorities have sufficient reason to believe that radio equipment covered by this Technical Regulation presents a risk to the health or safety of persons or to other aspects of public interest protection covered by this Technical Regulation, they shall carry out an evaluation in relation to the radio equipment concerned covering all relevant requirements laid down in this Technical Regulation. The relevant economic operators shall cooperate as necessary with the state market surveillance authorities for that purpose.

Where, in the course of the evaluation, the state market surveillance authorities find that the radio equipment presents a serious risk, the state market surveillance authorities shall without delay require the relevant economic operator to withdraw the radio equipment from the market and/or to recall it or to prohibit the radio equipment being made available on the market in accordance with the Methodology of taking restrictive (corrective) measures approved by Resolution of the Cabinet of Ministers of Ukraine No 1407 of 26 December 2011 (Official Bulletin of Ukraine, 2012, No 11, p. 402). The economic operator has the right to provide its explanations to the state market surveillance authority, according to Article 33 of the Law of Ukraine “On State Market Surveillance and Control of Non-Food Products”.

Where the market surveillance authorities find that the radio equipment does not comply with the applicable requirements (except in cases provided for the second indent of this point and the cases of formal non-compliance), the market surveillance authority shall without delay require the relevant economic operator to take during a stipulated period of time measures to bring the radio equipment concerned into compliance with the requirements set by this Technical Regulation.

Where the market surveillance authorities have found that the radio equipment does not comply with the requirements, whilst presenting a serious risk, the market surveillance authority shall apply the restrictive (corrective) measures provided for in the second indent of this point.

93. The economic operator shall ensure that all appropriate corrective action is taken in respect of all radio equipment referred to in point 92 of this Technical Regulation that it has made available on the market.

94. In case of the non-compliance of the radio equipment with the applicable requirements, the state market surveillance authorities shall indicate whether the non-compliance is due to either of the following:

failure of the radio equipment to meet the essential requirements;

shortcomings in the standards from the list of the national standards referred to in point 49 of this Technical Regulation.

Formal non-compliance of radio equipment

95. In addition to the reservations mentioned in points 92 to 94 of this Technical Regulation, the state market surveillance authorities shall require the relevant economic operator to put an end to the formal non-compliance concerned:

1) the mark of conformity with technical regulations has been affixed in violation of the requirements set out in points 58 to 63 of this Technical Regulation;

2) the mark of conformity with technical regulations has not been affixed;

3) the identification number of the designated body, where the conformity assessment procedure based on full quality assurance set out in Annex 3 is applied, has been affixed in violation of the requirements set out in point 62 of this Technical Regulation or has not been affixed;

4) declaration of conformity has not been drawn up;

5) declaration of conformity has not been drawn up correctly;

6) technical documentation is either not available or not complete;

7) the information referred to in points 24, 25 and 35 of this Technical Regulation is absent, false or incomplete;

8) information on the intended use of radio equipment, the declaration of conformity or usage restrictions as set out in points 26 to 28 of this Technical Regulation does not accompany the radio equipment;

9) requirements on identification of economic operators set out in point 48 of this Technical Regulation are not fulfilled;

10) the provisions of point 10 of this Technical Regulation are not complied with.

96. Where the formal non-compliance referred to in point 95 of this Technical Regulation persists, the state market surveillance authorities shall take all appropriate measures to restrict or prohibit corresponding radio equipment being made available on the market or ensure that it is withdrawn or recalled from the market.

Correlation table

97. The correlation table of the provisions of Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC and of this Technical Regulation is set out in Annex 7.

____________________

Annex 1
to the Technical Regulation

Module A
(internal production control)

1. Internal production control is the conformity assessment procedure whereby the manufacturer fulfils the obligations laid down in points 2 to 5 of this Annex, and ensures and declares on his sole responsibility that the radio equipment concerned satisfies the essential requirements of the Technical Regulation On Radio Equipment (hereinafter referred to as “Technical Regulation”) that apply to it.

Technical documentation

2. The manufacturer shall establish the technical documentation in accordance with points 66 to 69 of the Technical Regulation.

Manufacturing

3. The manufacturer shall take all measures necessary so that the manufacturing process and its monitoring ensure compliance of the manufactured radio equipment with the technical documentation referred to in point 2 of this Annex and with the relevant essential requirements set out in points 6 to 8 of the Technical Regulation.

Marking with the mark of conformity with technical regulations and declaration of conformity

4. The manufacturer shall affix the mark of conformity with technical regulations in accordance with points 60 to 63 and 65 of the Technical Regulation to each item of radio equipment that satisfies the applicable requirements of the Technical Regulation.

5. The manufacturer shall draw up a written declaration of conformity for each radio equipment type and keep it together with the technical documentation at the disposal of the state market surveillance authorities for 10 years after the last item of the radio equipment has been placed on the market. The declaration of conformity shall identify the radio equipment for which it has been drawn up.

A copy of the declaration of conformity shall be made available to the relevant state market surveillance authorities upon request.

Authorised representative

6. The manufacturer’s obligations set out in points 4 and 5 of this Annex may be fulfilled by his authorised representative, provided that they are specified in the mandate.

_____________________

Annex 2
to the Technical Regulation

Modules B and C

(type examination and conformity to type based on internal production control)

When reference is made to this Annex, the conformity assessment procedure shall follow Modules B (type examination) and C (conformity to type based on internal production control) of this Annex.

Module B
(type examination)

1. Type examination is the part of a conformity assessment procedure in which a designated body examines the technical design of the radio equipment and verifies and attests that the technical design of the radio equipment meets the essential requirements set out in points 6 to 8 of the Technical Regulation On Radio Equipment (hereinafter referred to as the “Technical Regulation”).

2. Type examination shall be carried out by assessment of the adequacy of the technical design of the radio equipment through examination of the technical documentation and supporting evidence referred to in point 3 of this Annex, without examination of a specimen (design type).

3. The manufacturer shall lodge an application for type examination with a designated body of his choice.

The application shall include:

the name and address of the manufacturer and, if the application is lodged by the authorised representative, his name and address as well;

a written declaration that the same application has not been lodged with any other designated body;

the technical documentation which shall make it possible to assess the radio equipment’s conformity with the applicable requirements of the Technical Regulation and shall include a description of methods and results of an adequate analysis and assessment of the risk(s). The technical documentation shall specify the applicable requirements and cover, as far as relevant for the assessment, the design, manufacture and operation of the radio equipment. The technical documentation shall contain, wherever applicable, the elements set out in Annex 4 to the Technical Regulation;

the supporting evidence for the adequacy of the technical design solution. That supporting evidence shall mention any documents that have been used, in particular where the relevant national standards have not been applied or have not been fully applied. The supporting evidence shall include, where necessary, the results of tests carried out in accordance with other relevant technical specifications by the appropriate laboratory of the manufacturer, or by another testing laboratory on his behalf and under his responsibility.

4. The designated body shall examine the technical documentation and supporting evidence to assess the adequacy of the technical design of the radio equipment.

5. The designated body shall draw up an evaluation report that records the activities undertaken in accordance with point 4 of this Annex.  Within the scope of its obligations as provided in point 8 of this Annex, the designated body shall release the content of that report, in full or in part, only with the agreement of the manufacturer.

6. Where the type meets the requirements of this Technical Regulation, the designated body shall issue a type examination certificate to the manufacturer. That certificate shall contain the name and address of the manufacturer, the conclusions of the examination, the aspects of the essential requirements covered by the examination, the conditions (if any) for its validity and the necessary data for identification of the assessed type of radio equipment. The type examination certificate may have one or more annexes attached.

The type examination certificate and its annexes shall contain all relevant information to allow the conformity of manufactured radio equipment with the examined type to be evaluated and to allow for in-service control.

Where the type does not satisfy the applicable requirements of this Technical Regulation, the designated body shall refuse to issue a type examination certificate and shall inform the applicant accordingly, giving detailed reasons for its refusal.

7. The designated body shall keep itself apprised of any changes in the generally acknowledged state of the art which indicate that the approved type may no longer comply with the applicable requirements of the Technical Regulation, and shall determine whether such changes require further investigation. If such changes require further investigation, the designated body shall inform the manufacturer accordingly.

The manufacturer shall inform the designated body that holds the technical documentation relating to the type examination certificate of all modifications to the approved type that may affect the conformity of the radio equipment with the essential requirements of the Technical Regulation or the conditions for validity of that certificate. Such modifications shall require an additional type examination of radio equipment and its approval in the form of an addition to the original type examination certificate.

8. Each designated body shall inform its designating authority concerning the type examination certificates and/or any additions thereto which it has issued or withdrawn, and shall, periodically or upon request, make available to its designating authority the list of such certificates and/or any additions thereto refused, suspended or otherwise restricted.

Each designated body shall inform the other designated bodies concerning the type examination certificates and/or any additions thereto which it has refused, withdrawn, suspended or otherwise restricted, and, upon request, concerning such certificates and/or additions thereto which it has issued.

Each designated body shall inform the central body of the executive power in the field of communications of type examination certificates it has issued and/or additions thereto in those cases where the standards from the list of the national standards have not been applied or not been fully applied.

The designating authority, relevant state market surveillance authorities and other designated bodies may, on request, obtain from the designated body a copy of the type examination certificates and/or additions thereto.

On request, the designating authority, relevant state market surveillance authorities and the central body of the executive power in the field of communications may obtain a copy of the technical documentation and the results of the examinations carried out by the designated body.

The designated body shall keep a copy of the type examination certificate, its annexes and additions, test records and technical information under point 1 of Annex 4 to the Technical Regulation 10 years after the radio equipment type examination has been carried out or until the expiry of the validity of that certificate.

9. The manufacturer shall keep a copy of the type examination certificate, its annexes and additions together with the technical documentation at the disposal of the state market surveillance authorities for 10 years after the last item of radio equipment has been placed on the market.

10. The manufacturer’s authorised representative may lodge the application referred to in point 3 of this Annex and fulfil the obligations set out in points 7 and 9 of this Annex, provided that they are specified in the mandate.

Module C
(conformity to type based on internal production control)

11. Conformity to type based on internal production control is the part of a conformity assessment procedure whereby the manufacturer fulfils the obligations laid down in points 12 to 14 of this Annex, and ensures and declares that the radio equipment concerned is in conformity with the type described in the type examination certificate and satisfies the requirements of this Technical Regulation that apply to such radio equipment.

Manufacturing

12. The manufacturer shall take all measures necessary so that the manufacturing process and its monitoring ensure conformity of the manufactured radio equipment with the approved type described in the type examination certificate and with the requirements of this Technical Regulation that apply to such radio equipment.

Marking with the mark of conformity with technical regulations and declaration of conformity

13. The manufacturer shall affix the mark of conformity with technical regulations in accordance with points 58 to 61 of the Technical Regulation to each item of radio equipment that is in conformity with the type described in the type examination certificate and satisfies the applicable requirements of this Technical Regulation.

14. The manufacturer shall draw up a written declaration of conformity for each radio equipment type and keep it at the disposal of the state market surveillance authorities for 10 years after the last item of radio equipment has been placed on the market. The declaration of conformity shall identify the radio equipment type for which it has been drawn up.

A copy of the declaration of conformity shall be made available to the relevant authorities upon request.

Authorised representative

15. The manufacturer’s obligations set out in points 13 and 14 of this Annex may be fulfilled by his authorised representative, provided that they are specified in the mandate.

_____________________

Annex 3
to the Technical Regulation

Module H
(conformity based on full quality assurance)

1. Conformity based on full quality assurance is the conformity assessment procedure whereby the manufacturer fulfils the obligations laid down in points 2, 12 and 13 of this Annex, and ensures and declares on his sole responsibility that the radio equipment concerned satisfies the essential requirements, laid down in points 6 to 8 of the Technical Regulation On Radio Equipment (hereinafter referred to as the “Technical Regulation”) that apply to it.

Manufacturing

2. The manufacturer shall operate a quality system for design, manufacture, inspection and testing of the manufactured radio equipment approved by the designated body as specified in point 3 of this Annex and shall be subject to surveillance as specified in points 8 to 11 of this Annex.

Quality system

3. The manufacturer shall lodge an application for assessment of his quality system with the designated body of his choice, for the radio equipment concerned.

The application shall include:

the name and address of the manufacturer and, if the application is lodged by the authorised representative, his name and address as well;

the technical documentation for each radio equipment type. The technical documentation shall contain, wherever applicable, the elements set out in Annex 4 to the Technical Regulation;

the documentation concerning the quality system;

a written declaration that the same application has not been lodged with any other designated body.

4. The quality system shall ensure compliance of the radio equipment with the requirements of the Technical Regulation that apply to it.

All the elements, requirements and the quality system provisions adopted by the manufacturer shall be documented in a systematic and orderly manner in the form of written policies, procedures and instructions. That quality system documentation shall permit a consistent interpretation of the quality programmes, plans, manuals and records.

The quality system documentation shall, in particular, contain an adequate description of:

the quality objectives and the organisational structure, responsibilities and powers of the manufacturer’s management with regard to design and radio equipment quality;

the technical design specifications, including standards, that will be applied and, where the relevant standards from the list of the national standards will not be applied in full, the means that will be used to ensure that the essential requirements of the Technical Regulation that apply to the radio equipment will be met;

the design control and design verification techniques, processes and systematic actions that will be used when designing radio equipment pertaining to the radio equipment type covered;

the corresponding manufacturing, quality control and quality assurance techniques, processes and systematic actions that will be used;

the examinations and tests that will be carried out before, during and after manufacture of radio equipment, and the frequency with which they will be carried out;

the quality records (inspection reports and test data, calibration data, reports concerning the qualifications of the personnel, etc.);

the means of monitoring the achievement of the required design and radio equipment quality and the effective operation of the quality system.

5. The designated body shall assess the quality system to determine whether it satisfies the requirements referred to in point 4 of this Annex.

The designated body shall presume conformity with the requirements referred to in point 4 of this Annex in respect of the elements of the quality system that comply with the corresponding requirements of the national standard which are identical to the relevant harmonised European standard.

The auditing team, appointed by the designated body, shall possess experience in quality management system and shall have at least one member experienced as an assessor in the relevant radio equipment field and radio equipment technology concerned, and knowledge of the applicable requirements of the Technical Regulation.

The quality system assessment shall include an assessment visit to the manufacturer’s premises.

The auditing team shall review the technical documentation referred to in the fourth indent of point 3 of this Annex to verify the manufacturer’s ability to identify the applicable requirements of this Technical Regulation and to carry out the necessary examinations with a view to ensuring compliance of the radio equipment with those requirements.

The designated body shall notify the manufacturer or his authorised representative of the decision.

The notification shall contain the conclusions of the audit and the reasoned assessment decision.

6. The manufacturer shall undertake to fulfil the obligations arising out of the quality system as approved and to maintain it so that it remains adequate and efficient.

7. The manufacturer shall keep the designated body that has approved the quality system informed of any intended change to the quality system.

The designated body shall evaluate any proposed changes and decide whether the modified quality system will continue to satisfy the requirements referred to in point 4 of this Annex or whether a reassessment is necessary.

The designated body shall notify the manufacturer of its decision. The notification shall contain the conclusions of the examination and the reasoned assessment decision.

Surveillance under the responsibility of the designated body

8. The purpose of surveillance is to make sure that the manufacturer duly fulfils the obligations arising out of the approved quality system.

9. The manufacturer shall, for assessment purposes, allow the designated body access to the design, manufacture, inspection, testing and storage sites of radio equipment, and shall provide it with all necessary information, in particular:

the quality system documentation;

the quality records as provided for by the design part of the quality system (results of analyses, calculations, tests, etc.);

the quality records as provided for by the manufacturing part of the quality system (inspection reports and test data, calibration data, reports concerning the qualifications of the personnel, etc.);

10. The designated body shall carry out periodic audits to make sure that the manufacturer applies and maintains the quality system and shall provide the manufacturer with an audit report.

11. In addition to periodic audits, the designated body may pay unexpected visits to the manufacturer. During such visits, the designated body may, if necessary, carry out radio equipment tests, or have them carried out, in order to check the proper functioning of the quality system. The designated body shall provide the manufacturer with a visit report and, if tests have been carried out, with a test report.

Marking with the mark of conformity with technical regulations and declaration of conformity

12. The manufacturer shall affix the mark of conformity with technical regulations in accordance with points 58 to 62 of the Technical Regulation and the identification number of the designated body referred to in point 3 of this Annex to each item of radio equipment that satisfies the applicable requirements of the Technical Regulation.

13. The manufacturer shall draw up a written declaration of conformity for each radio equipment type and keep it at the disposal of the state market surveillance authorities for 10 years after the last item of radio equipment has been placed on the market. The declaration of conformity shall identify the radio equipment type for which it has been drawn up.

A copy of the declaration of conformity shall be made available to the relevant authorities upon request.

14. The manufacturer shall, for a period ending 10 years after the last item of radio equipment has been placed on the market, keep at the disposal of the national authorities upon request:

the technical documentation referred to in the fourth indent of point 3 of this Annex;

the documentation concerning the quality system referred to in the fifth indent of point 3 of this Annex;

the change in quality system referred to in point 7 of this Annex (if any), as approved by the manufacturer;

the decisions and reports of the designated body referred to in points 7, 10 and 11 of this Annex.

15. Each designated body shall inform its designating authority of quality system approvals issued or withdrawn, and shall, periodically or upon request, make available to its designating authority the list of quality system approvals refused, suspended or otherwise restricted.

Each designated body shall inform the other designated bodies of quality system approvals which it has refused, suspended or withdrawn, and, upon request, of quality system approvals which it has issued.

Authorised representative

16. The manufacturer’s obligations set out in points 3, 7, 12 to 14 of this Annex may be fulfilled by his authorised representative, provided that they are specified in the mandate.

_____________________

Annex 4
to the Technical Regulation

CONTENTS 
of technical documentation

1. The technical documentation shall include at least the following elements:

1) a general description of the radio equipment including:

photographs or illustrations showing external features, marking and internal layout;

versions of software or firmware affecting compliance with essential requirements;

user information and installation instructions;

2) conceptual design, in particular manufacturing drawings, and schemes of components, sub-assemblies, circuits and other similar information;

3) descriptions and explanations necessary for the understanding of those drawings and schemes and the operation of the radio equipment;

4) the list of standards from the list of the national standards which are identical to the relevant harmonised European standards applied in full or in part to provide radio equipment with presumption of conformity with the essential requirements and, where those standards have not been applied, descriptions of the solutions adopted to meet the essential requirements of the Technical Regulation On Radio Equipment (hereinafter referred to as the “Technical Regulation”), including a list of other relevant technical specifications applied. In the event of partly applied standards, the technical documentation shall specify the parts which have been applied;

5) copy of the declaration of conformity;

6) where the conformity assessment module in Annex 2 to this Technical Regulation has been applied, a copy of the type examination certificate and its annexes as delivered by the designated body;

7) results of design calculations made, examinations carried out, and other relevant similar elements;

8) test reports;

9) an explanation in compliance with the requirements of point 20 and of the inclusion or not of information on the packaging in accordance with point 28 of the Technical Regulation.

2. The elements of technical documentation, referred to in the fourth indent of subpoint 1, in subpoints 4, 5, 6 and 9 of point 1 of this Annex, are to be executed in accordance with the law on the order of application of languages.

_____________________

Annex 5
to the Technical Regulation

DECLARATION OF CONFORMITY (No XXX)*

1. Radioequipment (product, type, batch or serial number): ______________________________________________________________

2. Name and address of the manufacturer or his authorised representative ___________________________________________________

3. This declaration of conformity is issued under the sole responsibility of the manufacturer.

4. Object of the declaration (identification of the radio equipment allowing traceability; it may include a colour image of sufficient clarity where necessary for the identification of the radio equipment)

_________________________________________________________________

5. The object of the declaration is in conformity with the requirements of such technical regulations:

Technical Regulation On Radio Equipment;

other technical regulation (where applicable).

6. References to the relevant standards used from the list of national standards or references to the other technical specifications in relation to which conformity is declared (with their identification number, version and date of issue) _______________________________________________________

7. Designated conformity assessment body

_________________________________________________________________

(name, identification number in the registry of designated bodies)

performed __________________________________________________________

(description of intervention)

and issued the type examination certificate No ______ of ___ __________ 20__ 
(in case a designated conformity assessment body was involved)

8. Where applicable, description of accessories and components, including software, which allow the radio equipment to operate as intended and covered by the declaration of conformity.

9. Additional information

Signed for and on behalf of _____________________________

_____________________________________________ ____ _________ 20__

(place and date of issue)

| _________________________________ (full name, function) | ___________________ (signature) |
| --- | --- |

*It is optional for the manufacturer to assign a number to the declaration of conformity.

_____________________

Annex 6
to the Technical Regulation

SIMPLIFIED DECLARATION 
of conformity

The simplified declaration of conformity referred to in point 27 of Technical Regulation On Radio Equipment shall be provided as follows:

hereby, (Name of manufacturer) declares that the radio equipment type (designation of type of radio equipment) is in compliance with Technical Regulation On Radio Equipment;

the full text of the declaration of conformity is available at the following internet address: __________________________________________________.

_____________________

Annex 7
to the Technical Regulation

CORRELATION TABLE
of the provisions of Directive 2014/53/EU of the European Parliament and of the Council of 16 April 2014 on the harmonisation of the laws of the Member States relating to the making available on the market of radio equipment and repealing Directive 1999/5/EC and of the Technical Regulation On Radio Equipment

| Provisions of the Directive | Provisions of the Technical Regulation |
| --- | --- |
| first part of Article 1 | first indent of point 1 |
|  | second indent of point 1 |
| second part of Article 1 | point 2 |
| third part of Article 1 | point 3 |
| fourth part of Article 1 | second indent of point 4 |
| subpoint 8 of preamble | third indent of point 4 |
| subpoints 1 to 17, 19 to 24 and 26 of first part of Article 2 | subpoints 1 to 24 of point 5 |
| subpoint 18 of first part of Article 2 | last indent of point 5 |
| subpoint 25 of first part of Article 2 |  |
|  | last indent of point 5 |
| second part of Article 2 |  |
| first part of Article 3 | point 6 |
| second part of Article 3 | first indent of point 7 |
| subpoint 10 of preamble | second to fourth indents of point 7 |
| third part of Article 3 | point 8 |
| Article 4 | point 9 |
| first part of Article 5 | point 10 |
| second part of Article 5 | point 11 |
| third and fourth parts of Article 5 | point 12 |
| fifth part of Article 5 |  |
| Article 6 | point 13 |
| Article 7 | point 14 |
| Article 8 | points 15 and 16 |
| Article 9 | points 17 and 18 |
| Article 10 | points 19 to 30 |
| Article 11 | points 31 and 32 |
| Article 12 | points 33 to 41 |
| Article 13 | points 42 to 46 |
| Article 14 | point 47 |
| Article 15 | point 48 |
|  | first indent of point 49 |
| Article 16 | second indent of point 49 |
| Article 17 | points 50 to 53 |
| Article 18 | points 54 to 57 |
| Article 19 | points 58 and 59 |
| Article 20 | points 60 to 63 |
| Article 21 | points 64 to 67 |
| Articles 22 to 24 |  |
| Article 25 | point 68 |
| first, second and ninth parts of Article 26 | point 69 |
| third to eighth, tenth and eleventh parts of Article 26 | points 70 to 77 |
| Article 27 |  |
| Article 28 | points 78 to 81 |
| Articles 29 to 32 | point 68 |
| Article 33 |  |
| Article 34 | points 82 to 86 |
| Article 35 | point 87 |
| Article 36 | points 88 and 89 |
| Article 37 |  |
| Article 38 | point 90 |
| Article 39 | point 91 |
| first, third and fifth parts of Article 40 | points 92 to 94 |
| second, fourth and sixth to eighth parts of Article 40 |  |
| Article 41 |  |
| Article 42 |  |
| Article 43 | points 95 and 96 |
| Articles 44 to 47 |  |
| Article 48 | point 3 of the Resolution that approved the Technical Regulation |
| Articles 49 to 52 |  |
|  | point 97 |
| Annex I | point 2 |
| Annex II | Annex 1 to the Technical Regulation |
| Annex III | Annex 2 to the Technical Regulation |
| Annex IV | Annex 3 to the Technical Regulation |
| Annex V | Annex 4 to the Technical Regulation |
| Annex VI | Annex 5 to the Technical Regulation |
| Annex VII | Annex 6 to the Technical Regulation |
| Annex VIII | Annex 7 to the Technical Regulation |

### _____________________